## Slide 1: Bootloaders for ARM
“You get NOTHING. GOOD DAY SIR!” -Willy Wonka
Notes: 1 min

## Slide 2: Recap: What’s a “Bootloader”?
When a system starts, it executes a bootloader to prepare the machine for use.
Not “magic” – just instructions to get things ready, like any other program
Typically serve to “bootstrap” the operating system (OS)
Sometimes come in multiple stages (first stage, second stage, …)
Vary in format and implementation by architecture and components
Some architectures have a standardized boot process, while others do not. The x86 line of processors (and its successor, x64) use a standardized process to ensure broad compatibility of operating systems across many manufacturers.
Notes: 4.5 min

## Slide 3: ARM: Instructions Not Included
ARM processors has very little standardization.
No standard memory map
No RAM/NVRAM/ROM standards
No driver or firmware standards
No boot standard, initialization, or formatting guidelines
In fact, ARM Classic has only two standards:
The trap table is at 0x00000000 or 0xffff0000 (hardware configured)
Execution starts at the beginning of the trap table
Notes: 4.5 min

## Slide 4: The Trap Table
Most processors (including x86 & ARM) use a trap table for hardware response.
ARM Classic Trap Table |  | “Akita” ROM Example | 
Offset | Description | Instruction | Explanation
0x00 | System Reset | b 0x34 | Jump to RESET routine (0x34)
0x04 | Undefined Instruction | ldr pc, [pc, #156] | Load address from 0xA8 into PC
0x08 | Supervisor Call | ldr pc, [pc, #156] | Load address from 0xAC into PC
0x0C | Prefetch Abort | ldr pc, [pc, #156] | Load address from 0xB0 into PC
0x10 | Data Abort | ldr pc, [pc, #156] | Load address from 0xB4 into PC
0x14 | (Reserved) | nop (mov r0, r0) | No operation (copy r0 over r0)
0x18 | Interrupt | ldr pc, [pc, #152] | Load address from 0xB8 into PC
0x1C | Fast Interrupt | ldr pc, [pc, #152] | Load address from 0xBC into PC
Note: destination is derived from PC, but processors prefetch.
On ARM, if offsetting from the PC, adding 12 bytes accounts for this.
Notes: Trap table – also referred to as “interrupt table”, “interrupt vector”, “interrupt vector table”, “hardware interrupt vector table…” because you know, one name is never enough, and we need something to argue about. 

## Slide 5: Initializing the ARM Processor
On boot, an ARM processor typically needs to…
Change to supervisor mode (x013)
Turn off THUMB instructions (usually)
Mask (disable) regular and fast interrupts
These can all be set in the Current Program Status Register (CSPR).
Mask Fast IRQ
Mask Regular IRQ
Disable THUMB
Set Supervisor Mode (0x13)
7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
1 | 1 | 0 | 1 | 0 | 0 | 1 | 1
Notes: --Walk through sample ARM bootloader

## Slide 6: Copy-On-Boot
Due to ARM’s lack of standardization, memory copies on boot are common.
mov r0, $source_addr // Load the source location
mov r1, $dest_addr // Load the destination location
mov r2, $last_addr // Get last addr to be copied
loop_start:
ldm r0!, {r3, r4, r5, r6, r7, r8, r9, r10} // load 8 bytes
stm r1!, {r3, r4, r5, r6, r7, r8, r9, r10} // store 8 bytes
cmp r0, r2
ble loop_start
LDM and STM increment the target register address by default.